## Slide 1: BETA STREAMFLOW DURATION ASSESSMENT METHOD (SDAM)
PRESENTED BY:
MATT MIKULECKY
REGULATORY TEAM LEADER
KANOPOLIS REGULATORY FIELD OFFICE

## Slide 2: PRESENTATION OBJECTIVES
INTRODUCTION TO SDAM
PURPOSE
DATA COLLECTION INDICATORS
INTENDED USE
POTENTIAL APPLICATIONS

## Slide 3: background
USEPA and USACE cooperative effort to develop a rapid assessment tool to help determine streamflow duration.
Six study regions have been established for SDAM development.
  Final SDAM Pacific Northwest
  Beta SDAM Arid West
  Beta SDAM Western Mountains
  Beta SDAM Great Plains
  Under development – Northeast and Southeast (including Puerto Rico & U.S. Virgin Islands)
  Under development – Alaska, Hawaii and Pacific Island U.S. Territories

## Slide 4: Study regions & status

## Slide 5: Sdam classifications
EPHEMERAL:
  Channels that flow only in direct response to precipitation .
  Water typically flows only during and/or shortly after large precipitation.
  The streambed is always above the water table and stormwater runoff is the primary source.

## Slide 6: Sdam classifications
INTERMITTENT (and at-least intermittent):
  Channels that contain sustained flowing water for only part of the year (typically during wet season).
  Streambed may be below the water table.
  Snowmelt from surrounding uplands provides sustained flow.
  Flow may vary greatly with runoff.

## Slide 7: Sdam classifications
PERENNIAL:
  Channels that contain flowing water continuously during a year of normal rainfall.
  Streambed located below the water table for most of the year.
  Groundwater typically supplies baseflow but may be supplemented by runoff/snow melt.

## Slide 8: Sdam indicators
THREE OVER-ARCHING INDICATOR CATEGORIES
Biological
Geomorphological
Regional location
Biological Geomophological Regional location

## Slide 9: Nine indicators
BIOLOGICAL
Richness of mayflies, stoneflies and caddisflies
Percent shading
Number of hydrophytic plant species
Absence of rooted upland plants in streambed

## Slide 10: Nine indicators cont’d…
GEOMORPHOLOGICAL
Bankfull channel width
Sinuousity
Floodplain and channel dimensions
Particle size or stream substrate sorting

## Slide 11: Nine indicators cont’d…
REGIONAL LOCATION INDICATOR
Northern or Southern Great Plains

## Slide 12: Intended use & applications
Used to support field classifications of streamflow duration at the reach scale
Applications may include but not limited to:
  Inform S404 Clean Water Act jurisdictional determinations
  Inform S404 Clean Water Act permit applications and evaluations
  Inform stream restoration, impacts and/or mitigation activities
Required field time approximately 2 hours

## Slide 13: Scale of assessment
Assessment reach scale = minimum 40 meters and maximum 200 meters
Determine reach by multiplying average bankfull width by 40
  Example: 2m x 40m = 80m assessment reach

## Slide 14: Data collection
Desktop reconnaissance
Onsite data collection using SDAM Field Form
Walk assessment reach and take bankfull width measurements
Collect percent shading data at 4 locations
Begin sketch of assessment reach on Field Form

## Slide 15: Data collection cont’d…
Evaluate other indicators
  Macroinvertebrates
  Assess channel and floodplain dimension
  Substrate assessment
  Record hydrophytic vegetation
  Assess upland plants growing in the channel
  Assess channel sinuosity
Complete sketch of assessment reach
Enter data into online web application to generate a streamflow duration classification

## Slide 16: Data collection tools
Field notebook
Field Forms
Maps & aerial photographs
GPS
Tape measure
Pocket rod or leveling rod/meter stick
Kick-net, small net and tray
Hand lens
Digital camera / smartphone
Shovel, soil auger, rock hammer
Sand gauge card
Densiometer
Field guides (plants and macroinvertebrates)

## Slide 17: Field form

## Slide 18: Online web application
Link:
SDAM Great Plains (shinyapps.io)

## Slide 19: Sdam links & contact
Beta Streamflow Duration Assessment Method for the Great Plains | US EPA
SDAM for Great Plains (arcgis.com)
Point-of-contact in Kansas City District: Matt Mikulecky, 816-389-3027
E-mail: matthew.j.Mikulecky@usace.army.mil

## Slide 20: questions